## Slide 1
MEDHA MEDITHON
2026
Transforming Healthcare Through Collaborative Innovation
Team Name: SAFEX
Problem Statement: CCTV-Based Fire Safety Compliance
Solution title: SAFEX AI — continuous fire-safety compliance from the cameras a hospital already has
Arya Dhanule
Vineet Shah | Team Lead
Meet Agrawal
Mohammad Ejaz Mehendi
Slide No 1
Vaishnavi Banait

## Slide 2
A hospital fire is not a building problem — it is a patient-movement problem.
  ICU, theatre and ward patients cannot self-evacuate; staff must move them through corridors that have to be clear.
  The failures that kill are mundane: a trolley parked in the escape route, a fire door wedged open, an extinguisher borrowed and never returned.
  Detectors are reactive. They tell you something is burning; none of them checks whether the building is still ready for it.
  Compliance is verified at periodic inspection — a corridor blocked on Monday is found in the quarterly audit, if at all.
  Paper checklists leave no evidence an inspector can trust and no record of how long a violation stood.
Problem Domain
MEDHA MEDITHON
2026
Slide No 2

## Slide 3
SAFEX AI — a compliance layer on the CCTV a hospital already owns.
  Continuously verifies four things detectors cannot: escape routes clear, fire doors closed, extinguishers present and reachable, exit signs lit.
  Detects flame and smoke on the same feeds — flame is called on the first frame it appears in.
  Key innovation: two independent readings per corridor — what the model can name, plus anything that appeared and stayed. Debris no classifier knows is still caught.
  False alarms are engineered out: nothing is a violation until it persists, and a person can never be read as smoke.
  Findings arrive on a Tuesday afternoon, when they can still be fixed — not during an evacuation.
Proposed Solution
MEDHA MEDITHON
2026
Slide No 3

## Slide 4
Existing CCTV in → fusion engine → compliance, alerts, evacuation, audit record out.
  Inputs: RTSP / IP / USB cameras, a phone or browser camera, an IoT sensor mesh, and fire-door contact switches.
  Vision: YOLOv8 flame / smoke / person; MOG2 background modelling for unknown obstructions; reference-image matching for doors and assets.
  Geometry: four clicks map each camera onto the floor plan, turning “41% obstructed” into “5.0 m of 8.4 m clear”.
  Engine: 5 Hz fusion into one hazard score per room, then incidents, spoken alerts and hazard-aware A* evacuation that descends the stair cores.
  Outputs: live dashboard, compliance report, hash-chained audit log, and advisory-only automated actions.
  Stack: Python, FastAPI, OpenCV, Ultralytics. No GPU, no database, no cloud — one command on a laptop.
Solution Architecture
MEDHA MEDITHON
2026
Slide No 4

## Slide 5
Already built and measured — this is a working system, not a concept.
  Runs on a laptop CPU: 24.5 FPS video with detection alongside it; a fire reaches CRITICAL with routes re-planned in 0.6 s.
  Deploys on the cameras already installed — no new hardware, no GPU, no cloud, no database.
  Risk — false alarms: measured. A face plus webcam noise used to read as smoke on 6 of 6 frames; it is now 0 of 10.
  Risk — lighting and camera drift: handled by per-pixel background modelling and a scene-change guard that says “camera view changed” instead of “corridor blocked”.
  Risk — blind spots: rooms with no camera and uncalibrated assets are printed in the report rather than quietly omitted.
  Regulatory: certified alarm panels, detectors and sprinklers are never actuated, silenced or delayed. SAFEX drives only its own fail-safe advisory devices.
Feasibility
MEDHA MEDITHON
2026
Slide No 5

## Slide 6
We did not prototype a demo — we shipped and measured a platform.
  Every capability in the brief is implemented end to end and verified with numbers we can reproduce live.
  Deep computer-vision work: detection, background modelling, reference matching and camera-to-plan homography — not an API call.
  Safety-engineering judgement: we treat a false alarm as a defect, gate every finding on persistence, and refuse to touch certified life-safety equipment.
  We document what the system cannot do as carefully as what it can — the quality an inspector actually needs from a monitoring vendor.
Why Our Team?
MEDHA MEDITHON
2026
Slide No 6

## Slide 7
Prototype/Solution Video
YouTube Link (unlisted): [PASTE YOUR LINK HERE]
Software / code repository: [PASTE YOUR GITHUB LINK HERE]
Run it yourself: pip install -r requirements.txt, then python run.py
The demo shows, in order:
  A three-storey hospital — 42 rooms, two stair cores, cameras on every floor.
  A kitchen fire on Level 2: CRITICAL in 0.6 s, incident opened, alert spoken, evacuation routed down Stair A to the assembly point.
  Compliance while it burns: blocked corridor, fire door held open, extinguisher access obstructed — score drops to 79.3.
  An automated action fired, and the fire panel refused by design.
  The compliance report, and an audit record proven intact after tampering.
MEDHA MEDITHON
2026
Slide No 7

## Slide 8
Thank You
MEDHA MEDITHON
2026
Slide No 8